## Slide 1: CERC Draft Sharing of ISTS Charges & Losses 2022 - 1st Amendment & Supplementary Amendment
Regulatory Affairs – India
10 Oct 2022

## Slide 2: Key Amendments - GNARE
No transmission charges for the use of ISTS shall be levied for the following GNA quantum (GNARE), for scheduling power from (i) REGS or RHGS based on wind or solar sources or (ii) ESS charged with REGS or RHGS based on wind or solar sources:
Where
• SDRG is drawl schedule (in MW) through ISTS under GNA from entities covered under subclauses (i) and (ii) of this Regulation in nth block.
• SDTG is total drawl schedule (in MW) under GNA through ISTS from all sources in nth block.
• ‘n’ is the nth time block
• T is number of time blocks in a month = 96 X number of days in a month
Provided that in case total drawl schedule (in MW) under GNA through ISTS from all sources, for nth time block, is less than 75% of Maximum schedule corresponding to GNA, the “SDTG” shall be taken as 75% of maximum schedule corresponding to GNA for the nth block.

## Slide 3: Impact
CERC Sharing Regulations 2020 – provided for 100% exemption for RE power.
The proposed formula does not provide 100% exemption, specially for OA/ C&I consumer procuring 100% RE
Suggested solution
GNARE (in MW)= GNA X (ADRG/ ADTG)
Where,
ADRG is the average of daily maximum actual schedule drawl (in MW) through ISTS under GNA from entities covered under subclauses (i) and (ii) of this Regulation
ADTG is the average of daily maximum actual total actual drawl schedule (in MW) under GNA through ISTS from all sources
 | C&I Solar (100 MW) | C&I Wind (100 MW) | C&I W+S Hybrid (100 MW) | Discom S+W+T (100+100+1000)
GNA (MW) | 100 | 100 | 200 | 1200
GNARE (MW) | 31.85 | 78.56 | 110.98 | 109.22
% Waiver | 31.85% | 78.56% | 55.49% | 9.10%

## Slide 4: 100% Solar Procurement
100 MW Solar PV
Chart: GNARE for Solar
GNA – 100 MW
GNARE – 31.85 MW
Suggestion 1 = GNA x Ave of Daily Peak RE Sch/ Ave of Daily Peak Total Sch
GNARE – 100 MW
Suggestion 2 = GNA x Ave of Daily Peak RE Sch
GNARE – 76.54 MW
MW | CERC Formula | Suggestion 1 | Suggestion 2
GNA | 100 | 100 | 100
GNARE | 31.85 | 100 | 76.54
% Waiver | 31.85% | 100% | 76.54%

## Slide 5: 100% Wind Procurement (100 MW WPP)
Chart: GNARE for Wind
100 MW WPP
GNA – 100 MW
GNARE – 78.56 MW
Suggestion 1 = GNA x Ave of Daily Peak RE Sch/ Ave of Daily Peak Total Sch
GNARE – 100 MW
Suggestion 2 = GNA x Ave of Daily Peak RE Sch
GNARE – 83.45 MW
MW | CERC Formula | Suggestion 1 | Suggestion 2
GNA | 100 | 100 | 100
GNARE | 78.56 | 100 | 83.45
% Waiver | 78.56% | 100% | 83.45%

## Slide 6: 100% Hybrid Procurement
Chart: GNARE for Hybrid
100 MW WPP + 100 MW Solar PV
GNA – 200 MW
GNARE – 111 MW
Suggestion 1 = GNA x Ave of Daily Peak RE Sch/ Ave of Daily Peak Total Sch
GNARE – 200 MW
Suggestion 2 = GNA x Ave of Daily Peak RE Sch
GNARE – 151.3 MW MW
MW | CERC Formula | Suggestion 1 | Suggestion 2
GNA | 200 | 200 | 200
GNARE | 110.98 | 200 | 151.29
% Waiver | 55.49% | 100% | 75.65%

## Slide 7: Discom Procurement
Chart: GNARE for Discom
100 MW WPP + 100 MW PV + 1000 MW TPP
GNA – 1200 MW
GNARE – 109.2 MW
Suggestion 1 = GNA x Ave of Daily Peak RE Sch/ Ave of Daily Peak Total Sch
GNARE – 176 MW
Suggestion 2 = GNA x Ave of Daily Peak RE Sch
GNARE – 151.3 MW MW
MW | CERC Formula | Suggestion 1 | Suggestion 2
GNA | 1200 | 1200 | 1200
GNARE | 109.22 | 176.30 | 151.29
% Waiver | 9.10% | 14.69% | 12.61%

## Slide 8
Thank you